## Slide 1: BASIC ELECTRONICS PROJECT AUTONOMOUS CAR MODEL
Student: Nguyen Thien Quang
Work Report
COLLEGE OF ENGINEERING
Instructor: M.s. Tran Le Trung Chanh

## Slide 2: Final Week
Work
Complete the code for autonomous car

## Slide 3: Complete the code for autonomous car
As the target before, the car will operate in 2 modes, one is the mode in which the car will be controlled by joystick and the other is it will run automatically with detecting and evading obstacles
Idea

## Slide 4: Complete the code for autonomous car
Flow chart for autonomous car
See more in DiagramForCar.drawio file

## Slide 5: Complete the code for autonomous car
Code implementation
See more in AutonomousCarNew folder

## Slide 6: Complete the code for autonomous car
Demo

## Slide 7: Complete the code for autonomous car
Problem
The car is able to run and the algorithm operated pretty well but the problem that emerges when testing the car’s direction moving is the car didn’t run in a straight line but run in a curve line when moving forward
Analyze
The cause of this problem is fairly easy to find. It turns out the motor on the right side of the car works with lesser performance than the leftside, then it will rotate slower and the result is the car was not moving to forward with a straight line but a curve line.

## Slide 8: Complete the code for autonomous car
Solution
As the requirement of the instructor before about adding encoder to the motor, they can use as a feedback of the motor’s rotation. So combine these encoder modules and using PID algoritm to control the speed of 2 motors the problem that emerge above can be solved.

## Slide 9: Complete the code for autonomous car
About PID algorithm
The PID algorithm is a widely used control algorithm that is used to regulate a process by adjusting a control variable. It stands for Proportional-Integral-Derivative, and it works by calculating an error signal that represents the difference between the desired setpoint and the current process variable, and then adjusting the control variable based on this error signal. By adjusting the gains of the proportional, integral, and derivative terms, the controller can be tuned to provide the desired response to changes in the process variable. The proportional gain determines the strength of the controller's response to the current error, the integral gain determines the strength of the controller's response to the accumulated error, and the derivative gain determines the strength of the controller's response to the rate of change of the error.

## Slide 10: Complete the code for autonomous car
PID implementation

## Slide 11: Summary
Process Achieved
Design an autonomous car model ( 4 wheels).
The wheels are omni wheels.
Using encoder motors and an obstacle detection sensor.
The car can be controlled by a wireless controller.
Using microcontrollers except for Arduino ecosystem.

## Slide 12: Summary
Advantage
The car operated well and can control in 2 modes with low latency response
Downside
Values that got from sensor is not so accurate because of the distortion when the car operates.
With PID implementation increased the accuracy when moving forward but the parameters to tune and rectify is still not close to get the car moves straight line completely.
The exterior design of the car still not so decent.

## Slide 13: Summary
Expansion and development
Using computer vision and machine learning is a good alternative way to replace sonicwave sensor in the car.
Add more batteries so the car will be able to run in more time.
Learn and calibrate about PID algorithm so the car will have better moving.

## Slide 14: Resources and references

## Slide 15: END OF PRESENTATION